## Slide 1: Transients identification basing on PDG (permanent downhole gauge) pressure data
Supervisors: Prof. Chunming Rong
Dr. Anton Shchipanov
Lejun Chen

## Slide 2: Outlines
Methods in last two decades
  Algorithms, detecting steps, user input, prerequisites
Experiments results of these methods
Summarization of these methods
Baseline methods that I developed
  A naive attempt need improvement
Job ahead
  Explore advanced methods: e.g. feature-based machine learning, predefine pattern recognition, etc.
  Web-application for testing real field data

## Slide 3: Methodology for analysis of PDG data (proposed by Athichanagorn 1999)
Outlier removal and denoising
Data reduction
Transient identification main task
Flow history reconstruction
Behavioural filtering
Data interpretation

## Slide 4: Methods investigated

## Slide 5: Time invariant spline wavelet
Athichanagorn (1999 & 2002)
Use wavelet multilevel signal decomposition
Detect algorithm:
  The wavelet modulus maxima at different levels of decomposition
  The characteristics of wavelet modulus maxima
    High level: signal singularities are group as a single singularity
    Low level: signal singularities and noise singularities both present
    Intermediate level: only signal singularities present detect this level
      Note: intermediate level may vary for different datasets

## Slide 6: Time invariant spline wavelet
Two criteria for pick up the transients
  need to chosen ( to pick which level to detect)
  : the length of shortest transient to be detected
  Slope threshold need to be chosen (for pick up the singularities)
  Improvement:
    Khong (2001)
      a statistical approach for choosing slope threshold

## Slide 7: Time invariant spline wavelet
Detecting steps:
  Determine which level should be used in the detection algorithm based on the desired resolution of the results.
  Choose a slope threshold to discriminate between singularities corresponding to new transients and noise singularities.
  Determine possible locations for starting positions of new transients by choosing wavelet modulus maxima whose detail signals are higher than the threshold and map the positions back to the original resolution.
  Check whether the slope extending from the singularity point forward is higher than the slope threshold and whether it deviates from the slope of data prior to the point of singularity.
  Determine the exact location of the beginning of a new transient by computing the intersection between a line that passes through the first two points in the new transient and another line passing through the last two points in the previous transient.

## Slide 8: Pattern-recognition approach
Thomas (2002)
  Identify aberrant transients
Olsen & Nordvedt (2005)
  Extend to identify normal transients

## Slide 9: Pattern-recognition approach
Two ways to determine the pattern for break points
  To predefine a pattern.  used by Olsen & Nordvedt
  To use a system learning process, like neural networks, to train the system for pattern recognition.

## Slide 10: Pattern-recognition approach
Three prerequisites
  Outliers must be removed.
  Denoising is recommended especially when the noise level is large.
  Not to use a noise filter that will seriously over smooth the transients.

## Slide 11: Four methods by Rai (2005)
Four methods:
  Haar wavelet (Stationary wavelet) perform similar as spline wavelet
  Savitzky-Golay polynomial smoothing filters
  Segmentation method significant improvements
  A variant of segmentation method

## Slide 12: Savitzky-Golay FIR smoothing filters
Basic idea:
  Denoising the data with Savitzky-Golay filter.
  Identify the breakpoints utilizing first-forth derivative.
  Threshold for choosing the peak is needed.

## Slide 13: Savitzky-Golay FIR smoothing filters
Algorithm for S-G filter:
  A type of digital filter that replaces each data value 𝑓𝑖 by a linear combination 𝑔𝑖 of itself and some number of nearby neighbours
  Similar with moving average, but not take the average
  To approximate the underlying function within the moving window not by a constant (whose estimate is the average), but by a polynomial of higher order.
  Note: Python has S-G filter library ready to use

## Slide 14: Savitzky-Golay FIR smoothing filters
Detecting steps:
  Find the peaks above a certain low threshold in the first derivative of pressure or rate data.
  A backward search is carried out for identifying the corresponding peaks in the second, third and fourth derivatives of the data.
  Interpolation between these locations is carried out by checking the slopes between each pair of locations to be higher than a certain value.

## Slide 15: Savitzky-Golay FIR smoothing filters
Smoothing and derivative calculation for different window size:
  Window size 21 window size 51
Better choice!

## Slide 16: Segmentation method
Detecting algorithm
  The first step is to collect a set of strategic points, by solving a sequence of maximum orthogonal (Euclidean) distance problems.

## Slide 17: Segmentation method
Detecting algorithm
  The second step is to calculate the area under each strategic point by considering the two other strategic points to its either side. The small or false breakpoints are then deflated using a very small area cut-off which is taken as a very small fraction of the highest area in the dataset.
  The third step is to screen further by checking the forward and backward slope. As a rule of thumb, if the forward slope is less then half the backward slope, the point is discarded. The slopes were obtained by least square fitting.

## Slide 18: Variation of Segmentation method
Basic idea
  Identifies the zeros in the flow rate.
  Between two consecutive zeros finds the peak using the segmentation approach.

## Slide 19: Data smoothing techniques
Nomura (2006)
Detection algorithm
(Treat as pressure fitting problem)
  Initial guess
  (from wavelet processing result)
  Insert break points
  Delete break points

## Slide 20: Data smoothing techniques
Applied to
Pressure data

## Slide 21: Smooth noise-robust differentiators
Pavel (2012)
Liu (2014)
Original Pressure data
First order derivative
Second order derivative

## Slide 22: Filter convolution
Suzuki & Chorneyko (2009)
Suzuki (2018)
  Improvement

## Slide 23: Filter convolution
Original signal Slope of pressure signal Indicator function of slope
Convolution Filter function
Detecting algorithm

## Slide 24: Filter convolution
Can be combined with noise deduction techniques
  Moving average and/or Derivative threshold
The size of window () is set to be the minimum transient interval we want to detect
Need 3-5 iterations of trial and error to determine the dp/dt threshold

## Slide 25: Comparison of results
Time invariant spline wavelet

## Slide 26: Comparison of results
Pattern-recognition

## Slide 27: Comparison of results
Savitzky-Golay FIR smoothing filters
(compare with wavelet)

## Slide 28: Comparison of results
Segmentation method

## Slide 29: Comparison of results
Variation of Segmentation method

## Slide 30: Comparison of results
Data smoothing

## Slide 31: Comparison of results
Filter convolution
(real oil well)
Interesting metrics:
The time duration of slop value larger than zero or small than zero

## Slide 32: Comparison of results
Filter convolution
(real gas well)
More challenging!

## Slide 33: Smooth noise-robust differentiators
Pavel (2012)
Liu (2014)
  Experiment result (synthetic data)

## Slide 34: Summarization(1)

## Slide 35: Summarization(1)

## Slide 36: Summarization(2)

## Slide 37: Summarization(3)
Main effort of these methods are contributed to distinguish the noisy data points from the real breakpoints.
The threshold needed fall into two categories:
  Used to filter noise:
    slope threshold, window size of S-G filter, tolerance
  The minimum transient interval we want to detect
    , 2

## Slide 39: Start Point Method
Basic idea:
(inspired by S-G filter method proposed by Rai)
  Denosing the raw data with S-G filter
  Identify as the breakpoints if:
    First order derivative > threshold_1
    Second order derivative > threshold_2
  Empirical threshold value: 2.5 * std

## Slide 40: Baseline methods:
Basic idea:
(inspired by filter convolution method proposed by Suzuki & Chorneyko )

## Slide 41
Algorithm | 
Point 1, point 2 are adjacent | 
: the first & second order derivative of point 1 | 
: the first & second order derivative of point 2 | 
: standard deviation of | 
: threshold tuning | 
: the initial value is | 
Start Point Real field data(smoothed): 404 detected, many points missed | 
if | 
point 2 is breakpoint | 
Baseline_1 | Baseline_2
if | if
if | if
point 2 is breakpoint | point 2 is breakpoint
 | =
Many points faulty because of noise | ! We only flip the sign of when two if statement are met
Baseline_1 + Baseline_2 = Baseline_improved Real field data: 116 (raw) or 69 (smoothed) detected, a few missed, a few faulty | 
Algorithm | 
Point 1, point 2 are adjacent | 
Start Point Real field data(smoothed): 404 detected, many points missed | 
point 2 is breakpoint | 
Baseline_1 | Baseline_2
point 2 is breakpoint | point 2 is breakpoint
Many points faulty because of noise | 
Baseline_1 + Baseline_2 = Baseline_improved Real field data: 116 (raw) or 69 (smoothed) detected, a few missed, a few faulty | 

## Slide 42: Start Point Method
Test with synthetic data
  Synthetic data
    6000 hours
    Pressure: 3519 measurements
    Flow rate: 95 measurements
  Ground truth: 45 (according to my judgement)
  Statistics plot for experiment result
    Noise threshold: 2.8*std points missed if threshold increase
    Total detected breakpoints: 71
    Points correct: 45
    Points faulty: 26
    Points missed: 0
detected
points
ground
truth

## Slide 43
Synthetic
Start point

## Slide 44: Start Point Method
Test with real field data (S-G)
  Real field data
    4070 hours
    Pressure: 29813 measurements
    Flow rate: 10191 measurements
  Ground truth: 60
  Statistics plot for experiment result
    With S-G filter
    Noise threshold: 3*std
    Total detected breakpoints: 404
    Points correct: ? (my next job)
    Points faulty: ? (my next job)
    Points missed: ? (my next job)
Left circle:
detected points
Right circle:
ground truth
points
correct
points
faulty
points
missed

## Slide 45: Start Point Method
Very noisy !
Data denosing
S-G filter parameters
window_length: 199
Polyorder: 3

## Slide 46
Points faulty
Points
missed
Denoised data
Start point

## Slide 47: Baseline Method
Test with synthetic data
  Synthetic data
    6000 hours
    Pressure: 3519 measurements
    Flow rate: 95 measurements
  Ground truth: 45 (according to my judgement)
  Statistics plot for experiment result
    Noise threshold: 2.4*std points missed if threshold increase
    Total detected breakpoints: 57
    Points correct: 45
    Points faulty: 12
    Points missed: 0
detected
points
ground
truth

## Slide 48
detected
points
ground
truth
Synthetic
Baseline

## Slide 49: Baseline methods:
Test with real field data
  Real field data
    4070 hours
    Pressure: 29813 measurements
    Flow rate: 10191 measurements
  Ground truth: 60 breakpoints
  Statistics plot for experiment result
Left circle:
detected points
Right circle:
ground truth
points
correct
points
faulty
points
missed
Without S-G filter
Noise threshold: 2*std
Total detected breakpoints: 116
Points correct: ? (my next job)
Points faulty: ? (my next job)
Points missed: ? (my next job)
With S-G filter
Noise threshold: 0.3*std
Total detected breakpoints: 69
Points correct: ? (my next job)
Points faulty: ? (my next job)
Points missed: ? (my next job)

## Slide 50
Raw data
Baseline

## Slide 51
Denoised
Baseline

## Slide 52: Baseline methods
Pros:
  Very good performance towards synthetic data
  Do not require denosing (however denoising can help to smooth extremely noisy points)
  Calculation cheap
Cons:
  Have difficulty for the data which is very noisy
  Difficult to filter the points where the flow rate decrease but not shut in
  Need threshold
  Performance is sensitive to threshold

## Slide 53: Baseline methods--Conclusion
About the S-G filter
  Helps with the extremely noisy data
  Increase the missed points if over smoothed
  The detected breakpoints are slightly different from the one without smoothing
The limitation of methods basing on derivatives
Difficult to get rid of noise threshold
The main reason for faulty detection

## Slide 54: Baseline methods--Discussion
The criteria for Ground_truth?
The criteria for points_correct?
  Should points closed to ground truth be classified as correct?
  Should points closed to each other be grouped as 1?
Is the flow rate always available?
  If so, we can use it to refine our detection basing on pressure data
  Or our scope is just using the pressure data?
The criteria for dominating multi-rate transient?

## Slide 55
A transient in 400-900 hours/synthetic data --My judgement for transients ?
Start point of
build up
Start point of
draw down
Zero flow rate
Zero flow rate
Start point of
Build up for next transient

## Slide 56: Job ahead (advanced methods)
Machine learning --- Feature extractions
  Inspired by the methods investigated
    first to forth order derivatives of pressure data, estimated noise(S-G filter method)
    the time duration the first derivative larger(or smaller) than zero, the first order derivative of the previous point (filter convolution method)
    Backward and forward slope of two adjacent detected breakpoints, slopes were obtained by least square fitting (segmentation methods)
  Feature selection criteria
    Realtime
    Case independent (require less or no expert use)
    The one that brings minor improvement will be discarded
    Computational cheap

## Slide 57: Job ahead (advanced methods)
Machine learning --- label
Generate Label
  Results from the baseline methods
  validate with flow rate

## Slide 58: Job ahead (advanced methods)
Machine learning –classical methods
  Split the data to train and test set following 80/20 rule
  Cross validation, K-means, etc.
  Experiment with different classifiers

## Slide 59: Job ahead (advanced methods)
Machine learning
  Pros:
    Higher accuracy
  Cons:
    More computation

## Slide 60: Job ahead (advanced methods)
Web application[10]
  Rest API
  API endpoint: Python flask web framework
  Front end: Javascript, CSS
  User interface(picture is from Anisa[10])

## Slide 61: Reference
[1] Athichanagorn, S. (1999). Development of an interpretation methodology for long-term pressure data from permanent downhole gauges.
[2] Olsen, S., Nordtvedt, J.E. (2005). Automatic Filtering and Monitoring of Real-Time Reservoir and Production Data.
[3] H. Rai. (2005). Analyzing rate data from permanent downhole gauges. MS report, Stanford University.
[4] Khong, C.K. (2001). Permanent Downhole Gauge Data Interpretation, MS report, Stanford University.
[5] Nomura, M. (2006). Processing and interpretation of pressure transient data from permanent downhole gauges.
[6] Suzuki, Satomi & Chorneyko, David. (2009). Automatic Detection of Pressure-Buildup Intervals From Permanent Downhole Pressure Data Using Filter Convolution. 10.2118/125240-MS.
[7] Pavel Holoborodko. (2009). Smooth noise-robust differentiators. http://www.holoborodko.com/pavel/numerical-methods/numericalderivative/smooth-low-noise-differentiators/deriv.
[8] Andrey Paramonov. (2015). Noise-robust smoothing filter. http://www.holoborodko.com/pavel/numerical-methods/noise-robustsmoothing-filter/.
[9] Liu Junrong, Yao Jun, Yu Weiqiang. (2016). Study of Identification Method of Transient Flow from Permanent Downhole Pressure Data. Journal of Southwest Petroleum University(Science Technology Edition)
[10] Anisa Zhurda, "Automated Well Monitoring: Machine Learning and Web Application," University of Stavanger, 2020.

## Slide 62
Thanks 
Any comments?

## Slide 63: Baseline methods:
Basic idea:
(inspired by filter convolution method proposed by Suzuki & Chorneyko )
Criteria for deciding breakpoints:
If there exists two adjacent points:
the sign of first order derivative are different
The difference of first order derivative is larger than a certain threshold
Then, the latter point is a breakpoint.
Note:
Empirical threshold value: 2.5 std
Works well with synthetic data, but not for real data because of NOISE!
(3) Set the sign of first order derivative of later point as same as the previous one, if the difference of slope between them is smaller than a threshold
to improve