## Slide 1: Transients identification basing on PDG (permanent downhole gauge) pressure data
Supervisors: Prof. Chunming Rong
Dr. Anton Shchipanov
Lejun Chen

## Slide 2: Outlines
Methods in last two decades
  Algorithms, detecting steps, user input, prerequisites
Experiments results of these methods
Summarization of these methods
Baseline methods that I developed
  A naive attempt need improvement
Job ahead
  Explore advanced methods: e.g. feature-based machine learning, predefine pattern recognition, etc.
  Web-application for testing real field data

## Slide 3: Methodology for analysis of PDG data (proposed by Athichanagorn 1999)
Outlier removal and denoising
Data reduction
Transient identification main task
Flow history reconstruction
Behavioural filtering
Data interpretation

## Slide 4: Methods investigated

## Slide 5: Time invariant spline wavelet
Athichanagorn (1999 & 2002)
Use wavelet multilevel signal decomposition
Detect algorithm:
  The wavelet modulus maxima at different levels of decomposition
  The characteristics of wavelet modulus maxima
    High level: signal singularities are group as a single singularity
    Low level: signal singularities and noise singularities both present
    Intermediate level: only signal singularities present detect this level
      Note: intermediate level may vary for different datasets

## Slide 6: Time invariant spline wavelet
Two criteria for pick up the transients
  need to chosen ( to pick which level to detect)
  : the length of shortest transient to be detected
  Slope threshold need to be chosen (for pick up the singularities)
  Improvement:
    Khong (2001)
      a statistical approach for choosing slope threshold

## Slide 7: Time invariant spline wavelet
Detecting steps:
  Determine which level should be used in the detection algorithm based on the desired resolution of the results.
  Choose a slope threshold to discriminate between singularities corresponding to new transients and noise singularities.
  Determine possible locations for starting positions of new transients by choosing wavelet modulus maxima whose detail signals are higher than the threshold and map the positions back to the original resolution.
  Check whether the slope extending from the singularity point forward is higher than the slope threshold and whether it deviates from the slope of data prior to the point of singularity.
  Determine the exact location of the beginning of a new transient by computing the intersection between a line that passes through the first two points in the new transient and another line passing through the last two points in the previous transient.

## Slide 8: Pattern-recognition approach
Thomas (2002)
  Identify aberrant transients
Olsen & Nordvedt (2005)
  Extend to identify normal transients

## Slide 9: Pattern-recognition approach
Two ways to determine the pattern for break points
  To predefine a pattern.  used by Olsen & Nordvedt
  To use a system learning process, like neural networks, to train the system for pattern recognition.

## Slide 10: Pattern-recognition approach
Three prerequisites
  Outliers must be removed.
  Denoising is recommended especially when the noise level is large.
  Not to use a noise filter that will seriously over smooth the transients.

## Slide 11: Four methods by Rai (2005)
Four methods:
  Haar wavelet (Stationary wavelet) perform similar as spline wavelet
  Savitzky-Golay polynomial smoothing filters
  Segmentation method significant improvements
  A variant of segmentation method

## Slide 12: Savitzky-Golay FIR smoothing filters
Basic idea:
  Denoising the data with Savitzky-Golay filter.
  Identify the breakpoints utilizing first-forth derivative.
  Threshold for choosing the peak is needed.

## Slide 13: Savitzky-Golay FIR smoothing filters
Algorithm for S-G filter:
  A type of digital filter that replaces each data value 𝑓𝑖 by a linear combination 𝑔𝑖 of itself and some number of nearby neighbours
  Similar with moving average, but not take the average
  To approximate the underlying function within the moving window not by a constant (whose estimate is the average), but by a polynomial of higher order.
  Note: Python has S-G filter library ready to use

## Slide 14: Savitzky-Golay FIR smoothing filters
Detecting steps:
  Find the peaks above a certain low threshold in the first derivative of pressure or rate data.
  A backward search is carried out for identifying the corresponding peaks in the second, third and fourth derivatives of the data.
  Interpolation between these locations is carried out by checking the slopes between each pair of locations to be higher than a certain value.

## Slide 15: Savitzky-Golay FIR smoothing filters
Smoothing and derivative calculation for different window size:
  Window size 21 window size 51
Better choice!

## Slide 16: Segmentation method
Detecting algorithm
  The first step is to collect a set of strategic points, by solving a sequence of maximum orthogonal (Euclidean) distance problems.

## Slide 17: Segmentation method
Detecting algorithm
  The second step is to calculate the area under each strategic point by considering the two other strategic points to its either side. The small or false breakpoints are then deflated using a very small area cut-off which is taken as a very small fraction of the highest area in the dataset.
  The third step is to screen further by checking the forward and backward slope. As a rule of thumb, if the forward slope is less then half the backward slope, the point is discarded. The slopes were obtained by least square fitting.

## Slide 18: Variation of Segmentation method
Basic idea
  Identifies the zeros in the flow rate.
  Between two consecutive zeros finds the peak using the segmentation approach.

## Slide 19: Data smoothing techniques
Nomura (2006)
Detection algorithm
(Treat as pressure fitting problem)
  Initial guess
  (from wavelet processing result)
  Insert break points
  Delete break points

## Slide 20: Data smoothing techniques

## Slide 21: Smooth noise-robust differentiators
Pavel (2012)
Liu (2014)
Original Pressure data
First order derivative
Second order derivative

## Slide 22: Filter convolution
Suzuki & Chorneyko (2009)
Suzuki (2018)
  Improvement

## Slide 23: Filter convolution
Original signal Slope of pressure signal Indicator function of slope
Convolution Filter function
Detecting algorithm

## Slide 24: Filter convolution
Can be combined with noise deduction techniques
  Moving average and/or Derivative threshold
The size of window () is set to be the minimum transient interval we want to detect
Need 3-5 iterations of trial and error to determine the dp/dt threshold

## Slide 25: Comparison of results
Time invariant spline wavelet

## Slide 26: Comparison of results
Pattern-recognition

## Slide 27: Comparison of results
Savitzky-Golay FIR smoothing filters

## Slide 28: Comparison of results
Segmentation method

## Slide 29: Comparison of results
Variation of Segmentation method

## Slide 30: Comparison of results
Data smoothing

## Slide 31: Comparison of results
Filter convolution
(real oil well)
Interesting characteristics:
The time duration of slop value larger than zero or small than zero

## Slide 32: Comparison of results
Filter convolution
(real gas well)
More challenging!

## Slide 33: Smooth noise-robust differentiators
Pavel (2012)
Liu (2014)
  Experiment result (synthetic data)

## Slide 34: Summarization(1)

## Slide 35: Summarization(1)

## Slide 36: Summarization(2)

## Slide 37: Summarization(3)
Main effort of these methods are contributed to distinguish the noisy data points from the real breakpoints.
The threshold needed fall into two categories:
  Used to filter noise:
    slope threshold, window size of S-G filter, tolerance
  The minimum transient interval we want to detect
    , 2

## Slide 38: Baseline methods:
Basic idea (a naive attempt):
Criteria for deciding breakpoints:
If there exists two points:
the sign of first order derivative are different
The difference of first order derivative is larger than a certain threshold
Then, the latter point is a breakpoint.
Note:
Empirical threshold value: 2.5 std
Works well with synthetic data, but not for real data because of NOISE!
(3) Set the sign of first order derivative of later point as same as the previous one, if the difference of slope between them is smaller than a threshold

## Slide 39: Baseline methods:
Test with synthetic data
  Synthetic data
    6000 hours
    Pressure: 3519 measurements
    Flow rate: 95 measurements
  Experiment result interpretation
detected
points
ground
truth
points
correct
points
faulty
points
missed

## Slide 40: Baseline methods
Test with synthetic data
  Total detected breakpoints: 57

## Slide 41: Baseline methods
Test with synthetic data

## Slide 42: Baseline methods
detected
points
ground
points
Test with synthetic data
  Ground truth: 45
  Statistics plot for experiment result
    Total detected breakpoints: 57
    Points correct: 45
    Points faulty:12
    Points missed: 0

## Slide 43: Baseline methods:
Test with real field data
  Real field data
    4070 hours
    Pressure: 29813 measurements
    Flow rate: 10191 measurements
  Experiment result interpretation
detected
points
ground
truth
points
correct
points
faulty
points
missed

## Slide 44: Baseline methods
Detected breakpoints: 72

## Slide 45: Baseline methods
Detected breakpoints: 72

## Slide 46: Baseline methods
Pros:
  Identify most of the main transients towards synthetic data
  Do not require denosing
  Calculation cheap
Cons:
  Have many faulty detections for real field data
  Difficult to filter the points where the flow rate decrease but not shut in
  Need threshold
  The value of threshold has a great influence to the performance

## Slide 47: Job ahead (advanced methods)
Machine learning --- Feature extractions
  Inspired by the methods investigated
    first to forth derivatives of pressure data, estimated noise(S-G filter method)
    the time duration the first derivative larger(or smaller) than zero (filter convolution method)
    Backward and forward slope of two adjacent detected breakpoints, slopes were obtained by least square fitting (segmentation methods)
  Feature selection criteria
    Realtime
    Case independent (require less or no expert use)
    The one that brings minor improvement will be discarded
    Computational cheap

## Slide 48: Job ahead (advanced methods)
Machine learning --- label
Generate Label
  Results from the baseline methods
  validate with flow rate

## Slide 49: Job ahead (advanced methods)
Machine learning –classical methods
  Split the data to train and test set following 80/20 rule
  Cross validation, K-means, etc.
  Experiment with different classifiers

## Slide 50: Job ahead (advanced methods)
Machine learning
  Pros:
    Higher accuracy
  Cons:
    More computation

## Slide 51
Thanks 
Any comments?

## Slide 52: An idea for using machine learning
How to extract features?
  Need careful analysis and investigation.
Some preliminary ideas
  Based on different algorithm, different features will be extracted.
    S-G filter: first to forth derivatives, maybe fifth needed, estimated noise, window size also matters?
    Filter convolution: first derivative, convolution value, estimated noise, the time duration the first derivative larger(or smaller) than zero, parameter of filter functions also matters??
    Maybe above two methods can be combined…
    Other methods?

## Slide 53: Questions
Which method to chose?
  Simplicity
  Accuracy
Our real case data
  Outlier removed?
  Denoised?
A naive thinking
  Use the reconstructed flow rate data (Anisa 2020) to identify the pressure transient

## Slide 54
2nd derivative
1st derivative
Original signal

## Slide 55: Challenges of PDG data
Pressure Transient Analysis (PTA)
  Need high frequency extraction
  1 pressure point per hour is more than enough
Rate Transient Analysis (RTA)
  Need low frequency extraction
  1,000 points extracted on a logarithmic time scale will be suitable for analysis

## Slide 56: Wavelet filtration

## Slide 57: Wavelet filtration

## Slide 59: Four methods by Rai (2005)
Name | Pros | Cons
Haar wavelet | same as spline wavelet | same as spline wavelet
Savitzky-Golay polynomial smoothing filters | identifying most of the true break points retaining fewer small and false break points screen out false break points in regions of high noise variance | difficulty in screening some smaller transients that are contained in the significant transients.
segmentation method | very effective in identifying all the significant break points retaining very few smaller transients the range of stopping criterion is relatively wide | 
a variant of segmentation method | perform as well as segmentation method | require both flow rate and pressure data

## Slide 60: Time invariant spline wavelet
Pros
  Effectively detect significant breakpoints
Cons
  Difficult to define universal criteria
    & Slope threshold
  Many false break points were detected
  Small transients were missed
  Require expert use
  Impossible for real time analysis

## Slide 61: Data smoothing techniques
Pros:
  Experiment result is effective
  Data driven and less subjective
  A consistent manner
Cons:
  Need to process data using the wavelet first
  More complex
  Two difficulties
    The insertion and deletion scheme is not guaranteed to produce the best result.
    The GCV minimization is not guaranteed to always produce a reasonable model due to the lack of local information.

## Slide 62: Smooth noise-robust differentiators
Pros
  Robust to noise
  Detect large transients as well as minor ones
  No need to denoising the data
  Simple algorithm

## Slide 63: Filter convolution
Pros:
  Robust to noise
  Perfectly accurate for oil well
Cons:
  More challenging for gas well
  Need 3-5 iteration to determine the criteria
  Need outliers removal and denoising before identification

## Slide 64: Baseline methods:
Start point:
  Empirical threshold value: 2.5 * std
  Synthetic pressure data real case pressure data